Elevator Buttons Application

Specifications
1. General purpose:
The robot should approach the outside buttons console of the elevator and press the
button chosen by the user.

Substasks
1.1. Detect the elevator buttons on the console.
1.2. Detect the location of each detected button.
1.3. Move the arm/s to the desired button location.
1.4. Press the button from (1.3).
1.5. Get feedback that the button was pressed correctly.
1.6 Encase the app with a full flow.

Schedule
07.10 – 29.10 (already done):
1.1 Detect the elevator buttons on the console
1.1.1 The detection model was built and converted to a RaYa template.
1.1.2 The detection model was implemented in a premilinery application.
1.1.3 The premilinery application was converted to a ‘skill’ format.

Capabilities – The robot can now detect the buttons and approach the console from a distance smaller than 1.5 meters.

30.10 – 13.11
1.2 Detect the location of each detected button
1.2.1 Detect the relevant points in space (x,y,z) of the chosen button.
Required: Calaibrated cameras

1.3 Move the arm/s to the desired button location
1.3.1 Check the accuracy of the arms and try to deal with errors.
Required: Calibrated arms

1.4 Press the button
1.4.1 See if we can work around the lack of gripper sensors and still press the buttons.
Required: Ideally, gripper sensors are required. In the meantime, we’ll try to work	around that